## Slide 1: Processing Near Memory for HPC and AI with HBM : AIA (Accelerate Indirect memory Access)
Shiju Li

## Slide 2: The Sparsity Challenge: Unlocking Performance in AI and HPC
The Problem: Data in the Real World is Sparse
  HPC Physics Simulations
  Sparse Linear Algebra (SpMV, SpMM, SpGEMM, …)
    Graph applications (BFS, PageRank, SSSP, ..)
    AI (LLMs, GNNs ..)
The Performance Penalty: Why Sparsity Hurts
  Irregular Memory Access
  The cycle of Inefficiency
    Big Cache Miss Ratio
    Memory Bandwidth is Wasted
    Execution Units Stall

## Slide 3: HPC Application

## Slide 4: Challenge of Sparsity for HPC application
Significant (52%) time is spent memory operations due to unstructured mesh operations
  Want to move only the data we need for computation
Instruction | Count | Percentage
Load | 6,775,030,849 | 18%
Branching | 6,063,697,707 | 16%
Integer Add | 5,334,155,682 | 14%
Array Indexing | 4,855,537,532 | 13%
Conditional | 3,299,248,274 | 9%
Store | 2,599,966,427 | 7%
Type cast | 1,959,938,043 | 5%
Sign extension | 1,541,094,404 | 4%
UME is a C++20 proxy based on a large computational physics application
  Approximates memory layout and indexing of an unstructured mesh
  Extracts an important computational kernel
    7 computation loops with indirect memory accesses (1 or 2 levels of indirections)

## Slide 5: Indirect (Irregular) Memory Access
=2
B[2]=7

## Slide 6: AIA - HBM (with Los Alamos National Lab.)
  Irregular memory access in parallel using multiple processing units and DRAM channels efficiently
  Only the resulting data is delivered  reduces data movement between processor and memory
BW efficiency

## Slide 7: Performance Benefic for UME w/ AIA

## Slide 8: Sparse Linear Algebra

## Slide 9: Sparse Matrix Multiplication and AI
  Pruning based Sparse Model require to accelerate sparse matrix multiplication performance
Specialized gather functions in sparse operation are needed
3 | 5 | 6
3 | 4 | 6
2 | 7 | 2
3 | 5 | 6
3 | 4 | 6
2 | 7 | 2
3 | 5 | 6
3 | 4 | 6
2 | 7 | 2
0 | 5 | 0
0 | 0 | 1
2 | 0 | 0
Dense
Matrix
Sparse
Matrix
Before Pruning
After Pruning
[ Hardware for Deep Learning @ HotChips 2023,
Presenter : Bill Dally (SVP of Research, NVIDIA) ]
Efficient Sparse Model
Models that deal with many modalities
[ Exciting Directions for ML Models and the Implications for Computing Hardware @ HotChips 2023,
Presenter : Jeff Dean (Chief Scientist, Google) ]
Dense Model
Sparse Model

## Slide 10: AIA and Sparse Matrix Multiplication
A | 0 | B | 0 | 0
0 | C | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | D
Only store non-zero value  capacity saving
Row Index
0 | 2 | 3 | 3 | 3 | 4
0 | 2 | 1 | 4
A | B | C | D
[ Sparse Matrix ]
[ Sparse Data Format ]
Column Index
Data
Row : 0
Column : 0
Data : A
A | 0 | B | 0 | 0
0 | C | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | D
a
b
c
d
e
a
A
X
+
c
B
X
b
C
X
e
D
X
X
Only multiply non-zero value  Computing Saving
[ Sparse Matrix Multiplication ]
0 | 2 | 1 | 4
Column Index
1
2
3
4
A | B | C | D
Data
a | c | b | e
A | B | C | D
X
AIA output
Indirect Memory Access
AIA
Sparse Matrix Multiplications use Sparse Format and Indirect Memory Access

## Slide 11: AIA and Sparse Matrix Multiplication on GPU
A | 0 | B | C
0 | 0 | 0 | D
0 | E | 0 | 0
0 | F | G | 0
A | 0 | B | C
0 | 0 | 0 | D
0 | E | 0 | 0
0 | F | G | 0
A | 0 | B | C
0 | 0 | 0 | D
0 | E | 0 | 0
0 | F | G | 0
0 | 0 | 0 | D
0 | E | 0 | 0
0 | F | G | 0
A | 0 | B | C
X
a | 0 | 0 | b
0 | 0 | c | D
d | 0 | e | 0
f | g | 0 | h
=
Aa |  |  | Ab
0 | 3 | 4 | 5 | 7
0 | 2 | 3 | 4 | 1 | 1 | 2
A | B | C | D | E | F | G
Matrix A Data
Matrix A Column Index
0 | 2 | 3 | 5 | 8
0 | 3 | 2 | 0 | 2 | 0 | 1 | 3
a | b | c | d | e | f | g | h
Matrix B Data
Matrix B Column Index
X
a | 0 | 0 | b
0 | 0 | c | D
d | 0 | e | 0
f | g | 0 | h
=
Bd |  | Be | 
X
a | 0 | 0 | b
0 | 0 | c | D
d | 0 | e | 0
f | g | 0 | h
=
Cf | Cg |  | Ch
+=
0 | 2 | 3 | 5 | 5 | 8
AIA output 1
1 | 2 | 3 | 0
0 | 1 | 2 | 3
Original Matrix A Row ID
Load balanced Matrix A row id
Bin #3
Bin #2
Bin #1
Bin #0
Mapping between GPU block id to matrix row id
i= block id
AIA_1 [2i]= a_row_ptr [d_map[i]]
AIA_1 [2i+1]= a_row_ptr [d_map[i]+1]
j=0,1,2
0 | 3
j = AIA_1 [2i] to AIA_1 [2i+1]
AIA_2[2j]= b_row_ptr[d_acol[j]]
AIA_2[2j+1]=b_row_ptr[d_acol[j]+1]]
AIA output 2
i=3
abdefgh
  Rows are grouped into bins, based on # of non-zero elements, different bins use different number of thread block and thread block size.
  Each bin can be processed independently, potentially allowing for better load balancing and resource utilization.

## Slide 12: GNN Workload: AIA+Pruning
Graph structure
0
1
2
3
4
6
7
5

## Slide 13: AIA improvement on SPGEMM for GNN Datasets
Notes: • AIA shows 20-60% improvement over CuSparse
• Without AIA shows 10-50% improvement over CuSparse
• Best AIA improvement: protein sage Consistent benefits across all configurations
• AIA provides additional 5-15% boost over baseline"""

## Slide 14: Pruning Impact on Accuracy

## Slide 15: AIA Speedup on GNN Training
Average 21.4%

## Slide 16: Summary
AI/HPC requires increasingly higher bandwidth and higher capacity memory
  Sparse data increase the complexity of data processing and more memory space
  We are researching various technologies to improve memory BW and usage with HBM
AIA, Processing Near Memory for HBM can alleviate memory bottleneck issues
  AIA with HBM could show the performance improvement for AI and HPC
  AIA needs to expand its application domain to become a more general technology
    We are looking for more AIA functions which are simpler, more general but powerful
    We are looking for more examples how AIA improves the performance for HPC and AI training and inferencing

## Slide 17
Booth
Literally.
#207
Meet the future of memory.
Just steps from the entrance.
Innovation starts here,

## Slide 18: GNN Training Time Comparison